## Slide 1
GENOVAATECH
LABS
PROJECT TITLE
AI-Enabled Underground Cable Fault Detection and Predictive Health Monitoring Using ESP32
Embedded Systems • IoT • Embedded AI • Electrical and Electronics
Predictive Maintenance Using Edge Intelligence
MONITOR · DETECT · PREDICT

## Slide 2
GENOVAATECH
LABS
01
Problem Statement
CABLE SENSING / EDGE AI / CONNECTED MAINTENANCE
FAULTS · DISTANCE · SAFETY · DOWNTIME
01 HIDDEN FAULT RISK
02 INCOMPLETE VISIBILITY
03 DELAYED MAINTENANCE
Failures are difficult to locate
Open- and short-circuit faults interrupt supply, while underground routing makes visual inspection slow, disruptive and uncertain.
DETECT • OPEN • SHORT
Signals must be interpreted together
Voltage drop, overcurrent, near-zero current and abnormal heating can be missed when each sensor is checked in isolation.
CORRELATE • V • I • °C
Raw readings do not guide the repair
Teams need the likely fault class, estimated distance, alert severity and event history before deciding where to inspect.
DECIDE • LOCATE • ACT

## Slide 3
GENOVAATECH
LABS
02
Abstract
CABLE SENSING / EDGE AI / CONNECTED MAINTENANCE
SENSE / ESTIMATE / CLASSIFY / CONNECT
01 INSTRUMENT THE CABLE
02 DIAGNOSE AT THE EDGE
03 CONNECT THE RESPONSE
Continuous electrical and thermal sensing
An ESP32 samples supply-side and load-side voltage, current and TMP117 temperature on a calibrated low-voltage cable test setup.
LIVE FEATURE STREAM
Rules and AI produce a faster diagnosis
The device detects open/short, overcurrent, sudden-current, near-zero-current and thermal anomalies; calibrated sensing estimates distance and AI is compared with a baseline algorithm.
BASELINE ↔ AI
Every event becomes visible and traceable
A Wi-Fi dashboard shows live values, fault type, distance, status and graphs; timestamps, readings and predictions are stored while local and dashboard alerts flag abnormal trends.
DASHBOARD • HISTORY • ALERTS

## Slide 4
GENOVAATECH
LABS
03
Proposed Solution
CABLE SENSING / EDGE AI / CONNECTED MAINTENANCE
MEASURE / DIAGNOSE / RESPOND
01 SENSOR FRONT END
02 EMBEDDED DIAGNOSIS
03 CONNECTED RESPONSE
Capture the cable’s condition
Voltage dividers, a current-sensing circuit and TMP117 feed the ESP32. A calibrated cable fixture safely injects simulated open- and short-circuit faults.
INPUT: VIN • VOUT • I • TMP117
Convert features into fault intelligence
The ESP32 filters readings, applies baseline thresholds, estimates fault distance and runs an AI classifier. Agreement and disagreement between both methods are retained.
OUTPUT: TYPE • DISTANCE • CONFIDENCE
Turn diagnosis into maintenance action
Wi-Fi publishes live status and graphs; event history records timestamps and sensor context; buzzer and dashboard alerts escalate faults and unusual cable-health trends.
ACTION: ALERT • INSPECT • REPORT
SENSOR FRONT END → ESP32 EDGE DIAGNOSIS → IoT DASHBOARD + LOCAL ALERT

## Slide 5
GENOVAATECH
LABS
04
Expected Output
CABLE SENSING / EDGE AI / CONNECTED MAINTENANCE
LIVE STATUS / DISTANCE / HISTORY / HEALTH
01 INSTANT DIAGNOSIS
02 MEASURED EVIDENCE
03 ACTIONABLE RECORD
A clear fault decision
The system reports Healthy, Open Circuit, Short Circuit, Overcurrent, Near-Zero Current or Thermal Anomaly, plus an estimated distance from the cable starting point.
FAULT TYPE • DISTANCE • STATUS
Live readings explain the decision
Supply voltage, load voltage, current and TMP117 temperature appear with trend graphs. AI prediction is displayed alongside the baseline result for comparison.
VIN • VOUT • CURRENT • TEMPERATURE
Alerts and history support follow-up
Each event stores a timestamp, sensor snapshot, estimate and prediction. Local buzzer and dashboard alerts flag immediate faults; health trends identify cables that warrant inspection.
TIMESTAMP • EVENT LOG • HEALTH FLAG
EXPECTED DASHBOARD FIELDS: FAULT | DISTANCE | V / I / °C | ALERT | TIMESTAMP